## Slide 1: Fundamentals of Steel Bridge Engineering
Lesson 5 – Shear in Girders
Notes: This presentation is part of the "Fundamentals of Steel Bridge Engineering" teaching aid, available at aisc.org/teachingaids. This set of (14) lessons was prepared by Frank Russo, PE, PhD and Michael Grubb, PE with support from the National Steel Bridge Alliance (NSBA) and AISC University Programs. For questions or comments on these presentations, please contact: AISC University Programs universityprograms@aisc.org

## Slide 2: Reference Materials
SBDH Vol 4 – Section 6.3.8
SBDH Vol 6 – Section 5.5
SBDH Vol 20 – Design Example 1
Notes: The following references are companion to this lesson:
SBDH Vol 4 – Section 6.3.8, Shear Strength
SBDH Vol 6 – Section 5.5 – Girder Web Design
SBDH Vol 20 – Design Example 1 – various sections

## Slide 3: Lesson Roadmap
Review of loads
  Influence lines, load placement, distribution factors
Basics of shear resistance
LRFD shear resistance
Design of webs, shear stiffeners, bearing stiffeners
Notes: This lesson briefly reviews live load placement for critical shear locations, reminds the user how to compute live load distribution factors for shear, but focuses mostly on the calculation of shear resistance of webs and the design of transverse shear and bearing stiffeners. Various example calculations are included.

## Slide 4: Loads – Key concepts

## Slide 5: Influence Line - Review
Chart: V at 0.0L, Span 1
| 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1 | 1.1000000000000001 | 1.2 | 1.3 | 1.4 | 1.5 | 1.6 | 1.7 | 1.8 | 1.9 | 2 | 2.1 | 2.2000000000000002 | 2.2999999999999998 | 2.4 | 2.5 | 2.6 | 2.7 | 2.8 | 2.9 | 3
 | 1 | 0.8757 | 0.7529 | 0.633 | 0.5175 | 0.41 | 0.31 | 0.21 | 0.13 | 0.06 | 0 | -0.05 | -0.08 | -0.1 | -0.11 | -0.1 | -0.08 | -0.06 | -0.04 | -0.02 | 0 | 0.0115 | 0.0193 | 0.0239 | 0.0257 | 0.0251 | 0.0225 | 0.0183 | 0.0129 | 0.0066 | 0
Influence line for shear at the end support of a 3-span bridge
Live load in Span 1 and 3 produces +V, a positive reaction at the left support.
  Truck load, Span 1
  Lane load, Spans 1 and 3
Live load in Span 2 produces –V, produces a negative reaction (uplift) at the left support.
Notes: The influence line for shear is plotted for a three-span bridge with span ratio of L – 1.2L – L, close to the span relationship of the NSBA Vol 20 Example 1 bridge.
One critical location for maximum shear is at the discontinuous end of the three-span beam. Maximum live load shear would be found by placing the HL93 uniform lane load in Span 1 and 3 and placing the truck or tandem load at the end of Span 1 as shown qualitatively. Negative shears, though non-critical in terms of the Strength Limit State can be obtained by loading the center span.
For Strength and Service Limit States, only the peak forces are needed. When it comes to the Fatigue Limit State, it is the range of shear, the difference between positive and negative values, that is of interest. Therefore it is important to understand, qualitatively, how the peak shears (positive or negative) are obtained for the Str and Ser Limit States and how a range of shear is determined for the Fatigue I / II limit State checks we will cover in future lessons.

## Slide 6: Influence Line - Review
Chart: V at 1.0L, Span 1
| 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1 | 1 | 1.1000000000000001 | 1.2 | 1.3 | 1.4 | 1.5 | 1.6 | 1.7 | 1.8 | 1.9 | 2 | 2.1 | 2.2000000000000002 | 2.2999999999999998 | 2.4 | 2.5 | 2.6 | 2.7 | 2.8 | 2.9 | 3
 | 0 | -0.124 | -0.247 | -0.367 | -0.483 | -0.592 | -0.694 | -0.788 | -0.871 | -0.941 | -1 | 0 | -0.051 | -0.083 | -0.1 | -0.103 | -0.096 | -0.082 | -0.062 | -0.04 | -0.019 | 0 | 0.012 | 0.019 | 0.024 | 0.026 | 0.025 | 0.023 | 0.018 | 0.013 | 0.007 | 0
Influence line for shear at the left side of Pier 1, Span 1
Live load in Spans 1 and 2 produces –V.
  Truck load in Span 1
  Lane load in both spans
Live load in Span 3 produces +V
Notes: Another critical location for shear is adjacent to interior piers. The influence line for shear at the 1.0L location of Span 1 is shown. Maximum negative shear is generated by placing the truck or tandem portion of the HL93 loading in Span 1 and lane loads in Spans 1 and 2.

## Slide 7: Calculation of Shear DF
Interior Girder
Exterior Girder
1 lane loaded
  Lever rule
Two or more lanes
  e*gint
Rigid cross section
1 lane loaded
2 or more lanes loaded
Notes: A reminder that the calculation of shears as shown in the prior influence line diagrams is not sufficient alone to predict the force in the beams. To find the live load and impact shear forces in particular beams, distribution factors are needed. Lessons 3 and 4 provide additional information on live loads, and methods of analysis, such as the use of distribution factors, for determining peak beam responses.
This slide simply repeats the equations and approach from LRFD Chapter 3. Empirical equations are provided for interior beams for the case of one and “two or more” lanes loaded. Exterior beams rely on a combination of the lever rule for one lane loaded, empirical corrections to the interior beam approach for two or more lanes loaded, and then also require engineers check the special analysis / rigid rotation model. The larger of the single and multi-lane DF’s applies to each interior and exterior beam, separately.

## Slide 8: Basics of Shear resistance

## Slide 9: Historical Approach to Web Design
Older bridges used thin webs and many stiffeners
Material was expensive and labor was inexpensive
Result = thin webs and many stiffeners
Notes: A photo of the I-64 riverside viaduct in Louisville, KY is used as an example of an older steel bridge and detailing common to the time of design and construction. Older structures commonly used relatively thin webs, to save weight, and made up for the loss of section by using a high number of stiffeners. Closely spaced stiffeners can be used to provide substantial strength enhancement to a thin web and this was a common approach for older structures (say pre 1990’s). Beginning in the 1990’s and continuing today, NSBA and the steel bridge industry in general reinforce the concept that least weight is NOT the least cost. A thin web, with a large number of stiffeners costs significantly more to fabricate than a thicker, heavier web, but with few stiffeners.
Photo Credit: Russo Structural Services

## Slide 10: Web Stiffeners Illustrated
An example of an older bridge where use of stiffeners and thin webs was common
① represent transverse intermediate shear stiffeners
② represent bearing stiffeners
③ represent cross-frame connection plates
①
②
①
①
③
②
③
Notes: An older bridge is shown to highlight the various types of transverse intermediate stiffeners that may be used on a steel bridge. Those details labeled ① are what are commonly called transverse intermediate shear stiffeners. These were used by the engineer to provide shear strength to a web whose capacity without stiffeners is inadequate to carry the shear demand. The structure, many decades old, is representative of common design and detailing practices of the past. Though no longer common, it was frequently the practice to design steel structures based on the least weight. This resulted in the use of relatively thin webs with a large number of shear stiffeners added. A more modern structure would have very few if any transverse intermediate shear stiffeners. It would instead use a thicker web. Those details labeled ② are the bearing stiffeners. These are the regions of the web subjected to high concentrated loads. The purpose of the bearing stiffeners is to prevent crushing and yielding of the web in the vicinity of those high concentrated loads. Those details labeled ③ are stiffeners where the cross-frame bracing is attached to the girders. These plates also serve as transverse intermediate shear stiffeners.
Photo Credit: Russo Structural Services

## Slide 11: Modern Approach
Use a limited number of stiffeners
Design webs so they “almost work” without stiffeners
Count on stiffeners already needed for bracing
Add stiffeners near high shear regions
Notes: There are three basic options for shear design of the girder webs.
An unstiffened design entails using a web thickness such that the shear buckling resistance of the web is equal to or greater than the factored shear demand. An unstiffened design would require only bearing stiffeners at the supports and diaphragm or cross-frame connection plates.
A partially stiffened design entails using a web 1/16 to 1/8 inch thinner than an unstiffened web design. This type of design will generally require transverse stiffeners in the first one or two bays between diaphragms at each end of each span.
A fully stiffened design entails designing the girder webs to be as thin as possible to meet the D/t limitations for girders without longitudinal stiffeners. The necessary shear capacity is achieved by providing enough transverse stiffeners to meet the shear demand due to dead and live loading. A minimum practical transverse stiffener spacing of 24 inches provides the upper limit to the shear capacity for a given web thickness and depth.
While the material costs do increase when unstiffened webs are used, there may be little change in the total fabrication cost of the fabricated girder. The amount of welding for the flange-to-web welds does not increase since minimum welds are generally adequate, thus limiting the increase in cost for the extra web material to the basic material cost of the steel. There may be a corresponding decrease in the size of the girder flanges when the thicker webs are used due to the increased web stiffness, and this decrease in flange material helps to offset the increased web material cost. Elimination of transverse stiffeners reduces labor costs associated with fabrication, fit-up and welding of the stiffener plates.
Other benefits associated with unstiffened webs are becoming increasingly important. If the girder is a painted design, minimizing the number of transverse stiffeners provides both a first cost benefit as well as a life cycle cost benefit by reducing the surface area requiring painting. The cost of bridge inspections may also be reduced since there are fewer details that require close inspection.
A fully stiffened design will provide the lightest possible web design but will also have the highest unit fabrication cost of the three options. An unstiffened design will result in the heaviest design of the three options but should have the lowest unit fabrication cost of the three. The partially stiffened option provides a trade-off between unit fabrication cost and material cost.
Throughout the late 1980s and the 1990s, the predominant opinion throughout the fabrication industry was that partially stiffened girder webs provided the optimum solution. However, the percentage of total girder cost related to fabrication labor cost has increased relative to the percentage of cost associated with material. Consideration should be given to the use of unstiffened girder webs for shorter spans. However, partially stiffened webs, especially for spans that only require one or possibly two stiffeners per panel near the interior supports, should still prove to be cost effective particularly for longer spans.
When comparing the cost of additional stiffeners to the cost of the extra web material associated with an increase in thickness, the stiffener unit material cost should be assumed to be approximately 5- 10 times the base material cost of the web to account for the additional fabrication required to weld the stiffeners to the girder.

## Slide 12: Fundamentals of Shear Behavior
In a Steel I- or box beam, shear is carried by the webs
Recall the distribution of shear stress on a small element
Vertical shear forces results in vertical AND horizontal shear stress
These can combine to produce principal tensile and compressive stresses
Notes: Recalling the classic strength of materials equation for shear stress, , only a small portion of shear is carried by the flanges, and it is simple and conservative to require that the webs be designed for the entire shear force. The same equation also shows a very small variation in from the junction of the web and flange and mid-height of the web, thus it is reasonable to assume a uniform distribution of the shear stress in determining the shear resistance of the web.
The distribution of shear stress on a small element shows the classic response of vertical shears needing to have corresponding horizontal shears to produce rotational equilibrium on a small element. The vectorial addition of the horizontal and vertical shears is equivalent to diagonal tension and compression forces / stresses on a rotated element
Image credit: Lincoln Electric
Recalling the classis strength of materials equation for shear stress, 𝜏=𝑉𝑄⁄𝐼𝑡, only a small portion of shear is carried by the flanges and it is simple and conservative to require that the webs be designed for the entire shear force. The same equation also shows a very small variation in 𝜏 from the junction of the web and flange and mid-height of the web, this it is reasonable to assume a uniform distribution of the shear stress in determining the shear resistance of the web.
The distribution of shear stress on a small element shows the classis response of vertical shears needing to have corresponding horizontal shears to produce rotational equilibrium on a small element. The vectorial addition of the horizontal and vertical shears is equivalent to diagonal tension and compression forces / stresses on a rotated element.

## Slide 13: Shear and Diagonal Tension
An element in pure shear is equal to an element in principal tension and compression rotated 45 degrees
When the shear stress reaches Fy/√3, i.e. 0.58Fy (or 0.6 Fy from AISC as an analogy), the material is considered to yield
This is the von Mises yield criteria
A thin web may buckle but does not lose the ability to carry diagonal tension.
  Think of the web being converted to diagonals in a truss
Notes: Continuing the discussion on stresses from the prior page, Mohr’s circle and the concepts of principle stress are important in understanding the relationship between shear and diagonal stresses. An element loaded in pure shear is equivalent to an element, rotated 45 degrees, and subjected to principle tension and compression.
When the shear stress reaches Fy / √3, written as 0.58Fy in AASHTO (or 0.6 Fy in AISC as a corresponding reference), the material is said to have yielded or reached its plastic shear resistance. The value of 0.58Fy is the maximum resistance of a web no matter how many stiffeners are added. The resistance can never exceed the basic resistance of the underlying web plate.
Returning back to the discussion on stresses, a thin web plate, subjected to orthogonal tension and compression forces, can buckle under the action of the compression forces. However, these buckles, which form normal to compression / parallel to tension, can be accommodated since the tensile resistance of the web is quite high compared to its compressive resistance. This shear resistance after buckling is called the postbuckling resistance, or the tension field action resistance, in the design specifications. It is like the web of a plate girder being converted into a pseudo-truss.

## Slide 14: Shear Resistance Assumptions
Webs carry all shear
Shear stress is uniform along the web height
Shear resistance is a stress (in ksi units) times the web area
Vn = f * Aweb where f is a resistance (in stress units) computed based on several parameters
Notes: Reiterating the basic assumptions:
Webs carry the full shear demand
The load is uniformly resisted by the full area of the web plate
Shear resistance is computed as a resisting stress, that depends on several parameters, multiplied by the area of the web.

## Slide 15: Shear Resistance Assumptions
For I-beams, some important parameters are:
Web dimensions, D and tw, and strength Fy
Stiffeners
  Present – Y / N?
  Spacing, do
Special modifications apply for tub girders and haunched beams
Notes: The important variables needed for the calculation of shear resistance include the web height and thickness, D and tw, the yield strength of the web, Fyw, whether or not stiffeners are provided and if provided, at what spacing, do.
For other special cases, there are additional modifications. These modifications for tub girders with inclined webs, and haunched / tapered girders with non-parallel flanges are addressed on the following two slides.

## Slide 16: Tub Girders
SBDH Vol 24
Shear Modifications, LRFD 6.11.9
Note: inclination of the web also produces lateral loads on the flanges
Notes: A sketch of the cross-section of a twin tub girder bridge design in SBDH Vol 24 is provided as an example of a typical steel tub girder. These commonly have inclined webs.
A common method of analysis for a beam like this is a line girder analysis. In a line girder analysis, the entirety of the cross-section is modeled simply by the moment of inertia of the cross-section. The line girder analysis does not “know” about any special characteristics of the beam such as the presence of the inclined webs. The analysis results in moments and shears being computed at specific points of interest. However, when it is time to check the resistance of the web, several important points must be addressed. Due to the incline, the vertical height of the web is different than the sloped height of the plate. It is the true sloped height that is used in the definition of the web area. Since the sloped web is used, the force along the slope is also needed. This is found simply by trigonometry. Note that the vertical force and inclined force have the same relationship as the vertical projection of the web and the inclined length. So computing an “amplified” shear using the equation shown is not truly an amplification as it is then checked with the sloped length of the web. The calculations can be done either way but because checks related to buckling relate to true and not projected dimensions, conversion of the vertical shear into an inclined force on an inclined plate is the correct and most common way to approach this situation.

## Slide 17: Shear in Haunched Sections, LRFD C6.10.1.4
R @ left
Loads in span, say DL for example
M
V
θ
V & M from girder analysis
Other values computed as shown
Notes: LRFD C6.10.1.4 addresses the case of inclined flanges. It provides an approach to compute the force in the flange itself, which is modified due to the slope, and also discusses corrections / reductions in shear in the web due to the vertical component of the flange force. Based on an approach found in Blodgett’s Design of Welded Structures chapter entitled “Bridge plate girders with variable depth” the method is a simple one that relies on the classic flexural stress equation f = M/S to compute the force Ph. All other calculations follow from that first result.

## Slide 18: LRFD Shear resistance

## Slide 19: Proportioning limits
The following relate to webs. These are not necessarily about shear, but important reminders
  D/tw ≤ 150 for webs without longitudinal stiffeners (LRFD 6.10.2.1.1-1)
  bf ≥ D/6 (LRFD 6.10.2.2-2)
  tf ≥ 1.1 tw (LRFD 6.10.2.2-3)
Notes: Though not related to shear resistance these limits are repeated as requirements that involve the web geometry.
For webs without longitudinal stiffeners, nearly all girders designed and fabricated in the United States, the maximum web slenderness is 150. If a longitudinal stiffener is used the slenderness is permitted to be 300.
A relationship between the web and flange geometry requires flanges to be at least one-sixth the web depth. This is more of a limit related to flange proportioning than to web proportioning.
Flange thickness must be greater than 110% of the web thickness, again a limit more related to the flanges than to the web.

## Slide 20: Shear – basic requirements
Roadmap for shear design
  6.5.4.2 Resistance factor, φ = 1.0
  6.10.9 Resistance, various articles
  6.10.11 Stiffeners, various articles
  6.10.3.3 Construction
Notes: Several important sections related to shear design are highlighted.
Article 6.5.4.2 is where all resistance factors, i.e.. the φ factors, are located. For shear, the resistance factor is 1.0.
Article 6.10.9 contains the various provisions for the resistance of the web. Sections are provided for webs with and without transverse stiffeners.
The design of stiffeners needed for shear is presented in 6.10.11. Stiffeners needed for shear in 6.10.11.1 and bearing stiffeners needed at points of concentrated loads, in 6.10.11.2.
Limits on the permissible behavior and capacity of webs during construction are found in 6.10.3.3. These will be covered in Lesson 7 on the Constructibility checks for steel structures.

## Slide 21: Shear Design Process, LRFD 6.10.9
Shear resistance is the same for homogeneous and hybrid sections
Process differs for webs with and without transverse shear stiffeners
For unstiffened webs, capacity is limited to buckling or yielding
For stiffened webs, the capacity is increased due to the stiffer web
Stiffened web has different procedures for interior and end panels
Interior panel procedure varies based on web to flange proportion checks
Notes: The shear resistance calculations for webs of I-beams are found in LRFD 6.10.9. The calculations have branches for stiffened and unstiffened webs.
For an unstiffened web there are only two outcomes, the web fully yields or it buckles, buckling being either elastic or inelastic.
For a stiffened web, AASHTO permits a resistance of either the yield strength as an upper bound or an additive contribution of buckling and post-buckling resistance. This is the process shown in the flowchart for a stiffened interior panel. For end panels with stiffeners, a different procedure is used, one that does not permit the addition of any postbuckling resistance because end panels, as will be shown in subsequent slides, are at the discontinuous end of a beam where the ability to develop and anchor the tension field component is not the same.
Finally, interior panels have one additional consideration, that is the potential for the flanges to be highly stressed in flexure at the same time they are trying to anchor the horizontal component of the diagonal tension field. When the web panel does not meet specific proportioning requirements, a drop in shear resistance is imposed as a means of handling shear and moment interaction in highly stressed regions.

## Slide 22: Unstiffened webs, LRFD 6.10.9.2
Capacity, φvVn is limited to buckling or yield resistance
Vn = CVp
Vp = Plastic shear resistance
= 0.58FyDtw
C = τcr / τy, a value between 0 – 1.0
Notes: An unstiffened web derives its entire resistance from the yield or buckling resistance of a web plate that is essentially simply supported at the top and bottom of the web plate (with some adjustment for moderate degree of rotational restraint) and loaded in shear. One of two possible failures is possible: for a stocky plate, yielding is possible. For more slender plates, buckling controls.
The capacity is therefore expressed as a percentage of the shear yield resistance of the section. A value C, ranging from 0-1.0, is computed and that is the decimal percentage of the shear yield resistance of the web of the unstiffened web. Even for webs that will eventually have stiffeners, i.e.. the partially stiffened webs discussed previously, the first step in all web designs is to compute the capacity of the unstiffened web so that regions needing stiffeners can be identified.

## Slide 23: Unstiffened Web Example
Notes: An unstiffened web is shown as an example. A shallow beam with only widely-spaced connection plates is an example of an unstiffened beam. Although there are stiffeners provided for the diaphragm connections, it will be shown in later slides that these are spaced too far apart to qualify as stiffeners. This beam is designed so that the unstiffened web has sufficient shear capacity.
Photo Credit: HDR

## Slide 24: The Parameter, C, LRFD 6.10.9.3.2
Vn = CVp
C is the ratio of shear buckling to shear yield resistance, varies 0 – 1.0
There are three regions
  No buckling
  Inelastic buckling
  Elastic buckling
Chart: C vs D/tw
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63 | 64 | 65 | 66 | 67 | 68 | 69 | 70 | 71 | 72 | 73 | 74 | 75 | 76 | 77 | 78 | 79 | 80 | 81 | 82 | 83 | 84 | 85 | 86 | 87 | 88 | 89 | 90 | 91 | 92 | 93 | 94 | 95 | 96 | 97 | 98 | 99 | 100 | 101 | 102 | 103 | 104 | 105 | 106 | 107 | 108 | 109 | 110 | 111 | 112 | 113 | 114 | 115 | 116 | 117 | 118 | 119 | 120 | 121 | 122 | 123 | 124 | 125 | 126 | 127 | 128 | 129 | 130 | 131 | 132 | 133 | 134 | 135 | 136 | 137 | 138 | 139 | 140 | 141 | 142 | 143 | 144 | 145 | 146 | 147 | 148 | 149 | 150

No shear buckling
Elastic
Buckling
Inelastic buckling
Limits of these regions depend on web yield strength and presence of stiffeners
Notes: This slide depicts the relationship between the parameter C and the slenderness of a web expressed as D/t. When buckling is prevented, C=1, i.e.. the full yield resistance of the web can be achieved. As the web becomes more slender, C decreases, linearly for inelastic buckling, and parabolically for elastic buckling.
The “anchor points” where the buckling regions meet depend on the yield strength of the web, and whether transverse stiffeners are provided and at what spacing.

## Slide 25: The Parameter, C
No shear buckling
Inelastic buckling
Elastic buckling
Chart: C vs D/tw
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63 | 64 | 65 | 66 | 67 | 68 | 69 | 70 | 71 | 72 | 73 | 74 | 75 | 76 | 77 | 78 | 79 | 80 | 81 | 82 | 83 | 84 | 85 | 86 | 87 | 88 | 89 | 90 | 91 | 92 | 93 | 94 | 95 | 96 | 97 | 98 | 99 | 100 | 101 | 102 | 103 | 104 | 105 | 106 | 107 | 108 | 109 | 110 | 111 | 112 | 113 | 114 | 115 | 116 | 117 | 118 | 119 | 120 | 121 | 122 | 123 | 124 | 125 | 126 | 127 | 128 | 129 | 130 | 131 | 132 | 133 | 134 | 135 | 136 | 137 | 138 | 139 | 140 | 141 | 142 | 143 | 144 | 145 | 146 | 147 | 148 | 149 | 150

No shear buckling
Elastic Buckling
Inelastic buckling
k=5 for unstiffened webs
More on k later
Notes: C is again presented on this slide and now with the values for D/t that separate the buckling regions. As mentioned on the prior slide, the break between regions depends on web yield strength and a parameter k. The parameter “k” is related to the presence or absence of stiffeners, and if present, their spacing.
For a web slenderness, , the web will not buckle, and can attain the full yield / plastic resistance, i.e.. C=1.0
At the other extreme, for a web with , these buckle elastically, and they have the lowest capacity.
In between is an inelastic region where webs meet the following slenderness requirement,
.
The intersection of the elastic and inelastic regions is set to intersect at C=0.8. Below C=0.8, behavior is elastic. Between C=0.8 and 1.0, behavior is inelastic. And when C=1.0, the web cannot buckle and will reach its full yield resistance.
C is again presented on this slide and now with the values for D/t that separate the buckling regions. As mentioned on the prior slide, the break between regions depends on web yield strength and a parameter k. The parameter “k” is related to the presence or absence of stiffeners, and if present, their spacing.
For a web slenderness, 𝐷/𝑡_𝑤 ≤1.12√(𝐸𝑘/𝐹_𝑦𝑤 ), the web will not buckle, and can attain the full yield / plastic resistance, i.e.. C=1.0
At the other extreme, for a web with 𝐷/𝑡_𝑤 >1.40√(𝐸𝑘/𝐹_𝑦𝑤 ), these buckle elastically, and they have the lowest capacity.
In between is an inelastic region where webs meet the following slenderness requirement,
1.12√(𝐸𝑘/𝐹_𝑦𝑤 )<𝐷/𝑡_𝑤 ≤1.40√(𝐸𝑘/𝐹_𝑦𝑤 ).
The intersection of the elastic and inelastic regions is set to intersect at C=0.8. Below C=0.8, behavior is elastic. Between C=0.8 and 1.0, behavior is inelastic. And when C=1.0, the web cannot buckle and will reach its full yield resistance.

## Slide 26: The Parameter, C
Chart: D/tw, dimensionless
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63 | 64 | 65 | 66 | 67 | 68 | 69 | 70 | 71 | 72 | 73 | 74 | 75 | 76 | 77 | 78 | 79 | 80 | 81 | 82 | 83 | 84 | 85 | 86 | 87 | 88 | 89 | 90 | 91 | 92 | 93 | 94 | 95 | 96 | 97 | 98 | 99 | 100 | 101 | 102 | 103 | 104 | 105 | 106 | 107 | 108 | 109 | 110 | 111 | 112 | 113 | 114 | 115 | 116 | 117 | 118 | 119 | 120 | 121 | 122 | 123 | 124 | 125 | 126 | 127 | 128 | 129 | 130 | 131 | 132 | 133 | 134 | 135 | 136 | 137 | 138 | 139 | 140 | 141 | 142 | 143 | 144 | 145 | 146 | 147 | 148 | 149 | 150

No shear buckling
Elastic buckling
Inelastic buckling
= 60 for 50 ksi unstiffened web
= 75 for 50 ksi unstiffened web
Notes: Additional detail on the parameter C is provided. Repeating the prior slide, this slide also present the equations for C.
A stocky web can reach the full yield resistance, therefore the ratio of the buckling resistance, to yield resistance, Vcr / Vp, is 1.0 i.e.. C=1.0
In the inelastic region, a straight line is used as a curve fit to experimental data. This straight line is a linear transition between C=1.0 and C=0.8, at which point the behavior transitions to elastic buckling. The linear equation for C is given as,
In the elastic region, buckling is predicted by a parabolic Euler-type curve and
Since we are still discussing unstiffened webs, the D/t “anchor points” where the behaviors transition are computed for k=5 and an assumed Fyw=50 ksi, the most common value for modern bridges. The value D/t=60 that ends the region of yield behavior is greater than all practical rolled shapes that are used for bridge girders. Thus, all rolled shapes webs of practical use will have their resistance based on a fully yielded web. Conversely, it is extremely rare and likely uneconomical to provide suck a stocky web in a plate girder bridge. Most plate girder webs fall into the inelastic or elastic range.
Additional detail on the parameter C is provided. Repeating the prior slide, this slide also present the equations for C.
A stocky web can reach the full yield resistance, therefore the ratio of the buckling resistance, to yield resistance, Vcr / Vp, is 1.0 i.e.. C=1.0
In the inelastic region, a straight line is used as a curve fit to experimental data. This straight line is a linear transition between C=1.0 and C=0.8, at which point the behavior transitions to elastic buckling. The linear equation for C is given as, 𝐶= 1.12/(𝐷⁄𝑡_𝑤 ) √(𝐸𝑘/𝐹_𝑦𝑤 )
In the elastic region, buckling is predicted by a parabolic Euler-type curve and 𝐶= 1.57/(𝐷⁄𝑡_𝑤 )^2 √(𝐸𝑘/𝐹_𝑦𝑤 )
Since we are still discussing unstiffened webs, the D/t “anchor points” where the behaviors transition are computed for k=5 and an assumed Fyw=50 ksi, the most common value for modern bridges. The value D/t=60 that ends the region of yield behavior is greater than all practical rolled shapes that are used for bridge girders. Thus, all rolled shapes webs of practical use will have their resistance based on a fully yielded web. Conversely, it is extremely rare and likely uneconomical to provide suck a stocky web in a plate girder bridge. Most plate girder webs fall into the inelastic or elastic range.

## Slide 27: Shear Buckling Coefficient, k, LRFD 6.10.9.3.2
k = a plate buckling coefficient
  do = transverse stiffener spacing
  D = web depth
For unstiffened webs, do = ∞, k becomes 5
AASHTO limits on do will be discussed later
Chart: Variation of k with do / D
| 0.5 | 0.75 | 1 | 1.25 | 1.5 | 1.75 | 2 | 2.25 | 2.5 | 2.75 | 3 | 3.25 | 3.5 | 3.75 | 4 | 4.25 | 4.5 | 4.75 | 5
Y-Values | 25 | 13.8889 | 10 | 8.2 | 7.2222 | 6.6327 | 6.25 | 5.9877 | 5.8 | 5.6612 | 5.5556 | 5.4734 | 5.4082 | 5.3556 | 5.3125 | 5.2768 | 5.2469 | 5.2216 | 5.2
If do/D > 3 the web is considered unstiffened. Widely spaced stiffeners are not effective
Notes: Th parameter k is a nondimensional plate buckling coefficient. It depends on factors such as the nature of loading (compression, bending, shear, combined stress), plate boundary conditions, and the aspect ratio (length to width) of the plate. The value for k in the AASHTO LRFD is the same as used in AISC equation (G2-5) for shear design.
k is computed based on an assumption of simply supported boundary conditions for the web as if the web was an isolated plate supported at 4 edges, the top and bottom flange, and transverse stiffener locations, by knife edge supports. Although not technically true, this is a reasonable and conservative assumption. Thus, the buckling coefficient becomes a function of the aspect ratio of the plate given by height, D, and spacing between transverse stiffeners, do. For an unstiffened web, do becomes infinity, the web is like a plate supported only at the top and bottom edges and subjected to shear. The value for k becomes 5 for an unstiffened web.

## Slide 28: Summary of Shear resistance, Unstiffened Webs
k = 5
Determine if behavior is yield or buckling
Compute C and Vp
Compute Vn
If Vu ≤ φVn, no stiffeners are needed. Otherwise, stiffeners are needed and must be located to provide the required shear strength
Notes: This slide summarizes the important concepts for an unstiffened web. The value k=5. Once k is found the engineer determines whether yielding or buckling (elastic or inelastic) is expected and computes a value for C. With C, the yield strength and area of the web, the resistance is determined. If the corresponding shear resistance exceeds the factored shear forces, no transverse stiffeners are needed. If the shear resistance is exceeded, stiffeners are required.
To reiterate the most common and economical design approach used for modern bridges. Size webs as follows.
Determine the shear forces at the critical locations, i.e.. support locations.
Size the web in 1/8 in. plate thickness increments. Do not use a plate less than ½ in. thick. Size the web to work as an unstiffened web.
Subtract 1/8 in. and determine how many stiffeners are needed and where along the span.
Determine if the weight savings of the web justifies the extra costs of the stiffeners. Stiffeners are on the order of 5 – 10 times as expensive, per pound, compared to the web material due to the individual cutting, grinding, fitting, and manual welding required for their fabrication and installation.

## Slide 29: Guided Walkthrough – Rolled beam shear resistance
Notes: A sample calculation for the resistance of a rolled beam is provided

## Slide 30: Example 1 - Capacity of a Rolled Shape
Scenario – a W27x94 used as a stringer
Assume 36 ksi steel
Stringer is unstiffened
Notes: The capacity of a W27x94 stringer in an existing truss bridge is computed. Rolled shape stringers are common in truss, arch and suspension bridges, i.e. bridges with parallel transverse floorbeams. They either rest on top or frame into the floorbeams. They support the deck and transfer load to the floorbeams. The capacity of this beam is being determined so that the load rating (capacity of the existing bridge) can be determined.

## Slide 31: W27 x 94 Section Properties
Total depth = 26.9 in.
Flange thickness = 0.745 in.
Net web = 26.9-2(0.745) = 25.41 in.
tw = 0.49 in.
D / tw = 51.9
Aw = 25.41(0.49) = 12.45 in.2
Notes: The section properties for a W27x94 are provided. Because shear resistance is associated with the web only, the net web height is computed. The thickness of the web is given. The D/t value is computed as is the area of the web. Properties for this section can be found in the AISC Steel Construction Manual.

## Slide 32: Compute capacity
Beam is unstiffened, k=5
D/tw < 71, C=1
φVn = (φ=1)(C=1)Vp = Vp
0.58FyAw = 0.58(36)(12.45) = 259 kips
Notes: The beam is unstiffened so k=5.
The web can fully yield if the web slenderness is less than
The Dt/w for this web was computed on the prior slide and is 51.9, less than 71, and C=1.0
The shear resistance is computed as 259 kips.
The beam is unstiffened so k=5.
The web can fully yield if the web slenderness is less than
1.12√(𝐸𝑘/𝐹_𝑦 )=1.12√((29000(5))/36)=71
The Dt/w for this web was computed on the prior slide and is 51.9, less than 71, and C=1.0
The shear resistance is computed as 322 kips.

## Slide 33: Stiffened Webs, LRFD 6.10.9.3
Two branches
  End panels
  Interior panels
    Two additional branches
Start with end panels due to commonalities with unstiffened webs
Notes: The process for stiffened webs is now presented. For stiffened webs, several additional questions must be asked and answered. Is the panel an end panel or an interior panel? If the panel is an interior panel, does the check for web area compared to average flange area result in a “yes or no” answer? Each of these questions are branches in the LRFD that result in separate equations being used for the resistance calculations.
Stiffened end panels have many similarities to unstiffened webs and the discussion of stiffened panels begins there.

## Slide 34: What is a Stiffened Web Panel?
A panel bounded by transverse stiffeners, spaced as below, and meeting stiffness requirements explored later in this lesson
do limits (LRFD 6.10.9.1)
  Interior panels without a longitudinal stiffener, 3D (k=5.55)
  Interior panels with a longitudinal stiffener, 2D (k=6.25)
  End panels with / without longitudinal stiffeners, 1.5D (k=7.22)
Chart: Variation of k with do / D
| 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1 | 1.1000000000000001 | 1.2 | 1.3 | 1.4 | 1.5 | 1.6 | 1.7 | 1.8 | 1.9 | 2 | 2.1 | 2.2000000000000002 | 2.2999999999999998 | 2.4 | 2.5 | 2.6 | 2.7 | 2.8 | 2.9 | 3
Y-Values | 25 | 18.8889 | 15.2041 | 12.8125 | 11.1728 | 10 | 9.1322 | 8.4722 | 7.9586 | 7.551 | 7.2222 | 6.9531 | 6.7301 | 6.5432 | 6.385 | 6.25 | 6.1338 | 6.0331 | 5.9452 | 5.8681 | 5.8 | 5.7396 | 5.6859 | 5.6378 | 5.5945 | 5.5556
Notes: A stiffened panel is defined as one where transverse (vertical) stiffeners are used to stiffen the web panel, decrease the aspect ratio of the web, and enhance its resistance. However, recall the discussion of the parameter k. For stiffeners infinitely far apart, k=5. Even for stiffeners less than an infinite distance apart there must be some constraints on spacing or else they serve no purpose.
AASHTO provides the following limits for stiffener spacing
Interior panels without a longitudinal stiffener, do/D max = 3, the resulting k=5.55.
Interior panels with a longitudinal stiffener, do/D max = 2, the resulting k=6.25.
End panels with or without longitudinal stiffeners, do/D max = 1.5, the resulting k=7.22.
Any panels containing stiffeners, but spaced farther apart than these limits, are considered unstiffened. Example. A plate girder has a 5 ft deep web. It has cross-frames 20 ft on center, and these are connected to the girder with transverse connection plates. These stiffeners are 4D on center and are not effective as shear stiffeners having violated the 3D limit above.

## Slide 35: Terminology
End panel – “a web panel adjacent to the discontinuous end of a girder”
Tension field action – “The behavior of a girder panel under shear in which diagonal tensile stresses develop in the web and compressive forces develop in the transverse stiffeners in a manner analogous to a Pratt truss.”
Notes: Terminology is introduced to aid in understanding the LRFD provisions. An end panel is a stiffened panel at the discontinuous end of a girder. Because there is only air to one side of this panel, i.e.. the beam is discontinuous, the forces developed in the web and flanges due to tension field action can not be anchored at this location. Capacity is limited in end panels to yield or buckling, like for unstiffened panels, but this time the buckling resistance reflects the presence of stiffeners
Tension field action is a resistance contribution only possible in stiffened interior panels. The onset of buckling is not the peak resistance of the web in shear, additional capacity can be mobilized in a post buckling response. This is called the tension field action contribution.

## Slide 36: Stiffened Panels
Stiffened End Panels
Adjacent to “free ends” of beams
Capacity is limited due to discontinuous web and flanges
  Anchorage of the tension field is not guaranteed at this location
Interior Panels
A panel bounded by continuous webs and flanges on each end
Notes: There are two types of stiffened panels: stiffened end panels and stiffened interior panels. As mentioned already, an end panel is at the discontinuous end of a beam. An example is the panel adjacent to an abutment or pier at an expansion joint location. The beam is discontinuous and the panel bounded by a bearing stiffener and the first transverse stiffener is called the end panel.
An interior panel is bounded on both sides by continuous web and flanges.

## Slide 37: Stiffened Panels
Unstiffened interior panels
Stiffened end panel
Stiffened interior panels
Notes: Using a girder elevation from Design Example 1 – SBDH Vol 20, the various panel types are highlighted
The end panel at the left end is between the bearing stiffener and the first interior stiffener. This spacing is back-calculated by a designer to meet the shear demands at this location.
The next panel is a stiffened interior panel measuring 16’-9” to the first cross-frame location. With the first stiffener located at the 7’-3” mark, the 16’-9” is the remaining distance. A designer first checks if this spacing is sufficient. If not, a stiffener is added in this distance, commonly by splitting the distance in half as a first trial.
Other interior panels are also present on the bridge. Near the center of the spans, where shear is low, no shear stiffeners are used, the only stiffeners attached to the web are those needed for cross-frame connections. And they are spaced further than 3D on center and thus do not even count as shear stiffeners.

## Slide 38: Stiffened End Panel
Unstiffened Webs
Stiffened End Panels
Capacity, φvVn is limited to buckling or yield resistance
Vn = CVp
Vp = Plastic shear resistance
= 0.58FyDtw
C = τcr / τy, a value between 0 – 1.0
k = 5, no stiffener
Capacity, φvVn is limited to buckling or yield resistance
Vn = CVp
Vp = Plastic shear resistance
= 0.58FyDtw
C = τcr / τy, a value between 0 – 1.0
k > 5 due to stiffeners
Notes: A stiffened end panel is limited in resistance to the lesser of the yield or buckling resistance. This is the same constraint as an unstiffened end panel. The only difference between the two, highlighted by the bottom row, is that in an unstiffened web the value for k=5 and for a stiffened end panel, k>5 due to the presence of stiffeners if they are 1.5D or less from the bearing stiffener.

## Slide 39: Stiffened End Panel
The only procedural difference between unstiffened panels and stiffened end panels is k > 5 for stiffened end panels.
Engineers choose a do so that the end panel has sufficient resistance
Notes: The equation for k is again presented as a reminder. The design of an end panel is done by selecting a value for do so that the shear resistance exceeds the factored force demands. It is either done by assuming a value for the stiffener spacing or by isolating do from the various equations needed for shear resistance. Assuming and checking the resistance is a common approach. The stiffener location is adjusted as needed to provide the required resistance. Given that do relates to k and k then influences C it can be cumbersome to try and isolate do from the various equations.

## Slide 40: C, Revisited
Note: k > 5 shifts the original web resistance curve to the right
The same “slenderness” web has increased resistance due to stiffeners
Chart: C vs D/tw
Notes: An additional change occurs when a stiffened web is used and k>5. The curves for C shift to the right from the previous curves based on k=5. The result is for a given D/t a higher shear resistance is attained in a stiffened web. Alternately, equal shear resistance can be obtained with a more slender stiffened web
This again relates to the design process for a girder web. Reinforcing prior discussions, it is common and generally economical to either use an unstiffened web, or design the web as it is unstiffened, thin the web by approximately 1/8-in. (increasing D/t in the process) and then adding a stiffener, shifting the C curves to the right and raising the shear resistance for a given D/t value.

## Slide 41: Stiffened Interior Panels, LRFD 6.10.9.3.2
Interior panels have the highest possible resistance
Buckling is not the limit of capacity, post-buckling resistance, i.e.. tension field action, is permitted
Notes: The ultimate shear resistance of stiffened webs may be taken as the additive combination of the shear buckling resistance with a representation of the shear postbuckling resistance from Basler’s (1961) seminal research.
Tension field action assumes that the web develops tensile postbuckling stresses (i.e., a tension field) along a diagonal in the web panels as shown, in addition to the shear buckling stresses. In determining the slope of this tension field, Basler assumes that only an effective band, s, takes part in transmitting the additional tension (i.e.., the flanges are assumed to provide zero anchorage to the theoretical tension field). The maximum resistance is obtained when yielding occurs due to the combination of the tension field stress plus the initial web shear buckling stress. The angle θ is determined to maximize the predicted postbuckling contribution. Although there are some inconsistencies in Basler’s theory and the equations he developed, and now are used in AASHTO, Basler (1963) acknowledges this inconsistency, and explains that the flanges are actually not loaded to the extent required by his theory in physical tests. Nevertheless, he argues that his theory still provides an acceptable characterization of I-girder shear resistances.

## Slide 42: Interior Panels
Tension field action may be limited by cross-section proportion constraints
If
  Full tension field can be achieved
  Otherwise, a reduction is applied
Notes: Basler’s work showed that when comparing the area of the web to the average area of the flanges, a result <= 2.5 resulted in the full tension field being able to be mobilized and resisted. Note that the “2” in the numerator comes from inverting a fraction in the denominator which is the average of the flange areas. Basler’s theory relies on a truss-type behavior, the horizontal component of the tension band being taken as thrust in the flanges. The need to limit the web and flange area ratio was so that the horizontal component of the diagonal tension field, when added to flexural forces in the flanges, does not result in a failure of the cross-section due to combined loading.

## Slide 43: Shear resistance, Interior Panels
Full tension field action
Vp*C = buckling resistance
+ … = post-buckling resistance
Reduced tension field action
Vp*C = buckling resistance
+ … = post-buckling resistance
Additional do/D in denominator = reduction due to web and flange proportions
Notes: The LRFD equations for shear resistance contain two terms. The first term inside the brackets, C, is the buckling resistance of the web. To that is added a postbuckling resistance. The equation for reduced tension field action contains an additional term in the denominator to capture the interaction effects of shear and flexure in highly loaded panels.
The above idealizations are only a very simplified representation of the true web response. Numerous additional web shear failure theories have been postulated since Basler’s original research. The large number of these idealizations in itself is evidence of the fact that the corresponding behavior is complex and tends to defy explanation by basic plane stress strength of materials models. Nevertheless, the ability of the LRFD equations to provide a reasonable prediction of experimental test results is irrefutable. See SBDH Vol 4 Section 6.3.8 for additional detail on these shear models.

## Slide 44: Guided Walkthrough – SBDH Example 1 Shear resistance

## Slide 45: Example 2 – SBDH Example 1
Compute loads and capacities for selected locations from SBDH Example 1
Notes: A portion of the SBDH Vol 20 Example 1 bridge is checked for shear using the stiffened panel checks presented on previous slides.

## Slide 46: Calculation of Shear DF
Interior Girder
(SBDH Vol 20, 7.2.1.1)
Exterior Girder
(SBDH Vol 20, 7.2.1.2)
Lever rule, 0.900 lanes
Two or more lanes, 0.866 lanes
Rigid cross section
  1 lane, 0.750 lanes
  2 lanes, 0.950 lanes
  3 lanes, 0.829 lanes
1 lane loaded
2 or more lanes loaded
lanes
Notes: As a reminder, factored shear force effects are needed. This includes dead load forces such as DC1, DC2, and DW, as well as the moving live load results; these also require a distribution factor.
For an interior beam, both single and two or more lane loaded values are computed, the two or more lane value controls. For an exterior beam, the lever rule is checked for a single lane, an empirical correction to the interior beam value is made for two or more lanes loaded, and then the rigid rotation model is checked for one, two, and three lanes. The highest value for an exterior beam is less than for an interior beam, the interior beam governs for shear.

## Slide 47: Shear Forces
Forces from each load type are shown
DC1 = noncomposite DC loads (beam, slab, etc.)
DC2 = composite DC loads (barriers)
DW = future wearing surface
+LL+IM = positive shears at any tenth point from moving load analysis
-LL+IM = negative shears at any tenth point from moving load analysis
Notes: The shear forces at tenth point locations are plotted. Note that the dead load forces plot as sloped straight lines, these are uniformly distributed loads and the shear plots accordingly. The live load shears are curvilinear and also have positive and negative values at each tenth point. Recall earlier in this lesson when influence lines were plotted for the left support and for the left side of the beam at Pier 1. These influence lines have positive and negative ordinates, meaning positive or negative shear can be generated. Similar influence lines can be plotted for all tenth points, generating the range of live loads at any specific tenth point. The live load forces come from placement of the truck and lane loads on the influence lines, applying impact to the truck portion of the load model, and then applying the controlling live load distribution factors to the sum of the forces. Those distributed force effects are plotted here to represent the forces in the beam to be combined with the permanent load force effects.

## Slide 48: Example Strength Load Combination
STR I Limit State
  Vu = ηDηRηI[γDC(DC1+DC2)+γDW(DW)+γLL(LL+I)]
  Vu = 1.0[1.25(87+13)+1.5(13)+1.75(139)] = 388 kips
This process repeats for all tenth points and other points of interest
This calculation helps determine where transverse shear stiffeners are needed
Notes: A sample calculation is provided for the shear at the left end of the end span. The STR I load combination is used. A 1.25 factor applies to DC loads (DC1 and DC2), the 1.5 factor applies to DW, and a 1.75 factor applies to live load. The factored shear at the left abutment / left support is 388 kips.

## Slide 49: STR I Shear Envelope
Factored shear forces at each tenth point are shown
Interior girder controls
For shear, sign is not relevant
Notes: The process is repeated for all tenth points. Only the algebraically highest shear at any tenth point is relevant. Shear design uses unsigned values; a positive or negative value does not influence the design. That is why the entire envelope for all tenth points is not shown.
Note that in continuous beams, the shear is highest adjacent to interior supports, for this example approximately 545 kips on either side of the support. The value from the prior slide, 388 kips, is at the free end support.

## Slide 50: Unstiffened Web Capacity
E = 29000 ksi
Fyw = 50 ksi
D = 69 in.
tw = 0.5 in.
D/tw = 138 > 75
Buckling is elastic
Chart: C vs D/tw
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63 | 64 | 65 | 66 | 67 | 68 | 69 | 70 | 71 | 72 | 73 | 74 | 75 | 76 | 77 | 78 | 79 | 80 | 81 | 82 | 83 | 84 | 85 | 86 | 87 | 88 | 89 | 90 | 91 | 92 | 93 | 94 | 95 | 96 | 97 | 98 | 99 | 100 | 101 | 102 | 103 | 104 | 105 | 106 | 107 | 108 | 109 | 110 | 111 | 112 | 113 | 114 | 115 | 116 | 117 | 118 | 119 | 120 | 121 | 122 | 123 | 124 | 125 | 126 | 127 | 128 | 129 | 130 | 131 | 132 | 133 | 134 | 135 | 136 | 137 | 138 | 139 | 140 | 141 | 142 | 143 | 144 | 145 | 146 | 147 | 148 | 149 | 150

=60
Notes: The field section being checked has a 69 x 0.5 in web. The capacity of the unstiffened web is computed using equations presented in this lesson. The D/t of 138 is plotted and is in the range of elastic behavior. It is to the right of the transition between inelastic and elastic buckling, D/t of 75. The equation for elastic C is used and C=0.239.

## Slide 51: Unstiffened Web Capacity
kips
Vn = Vcr = CVp = (0.239)(1001) = 239 kips
Shear stiffeners are required when Vu > 239 kips
Note: capacity of a 5/8” web = 470 kips, a 3/4” web = 807 kips
Notes: With C=0.239, the next calculation is to compute Vp, 1,001 kips. The nominal resistance of the unstiffened web is 239 kips. Since φ=1, the factored resistance is similarly 239 kips.
Recall that the shear at the abutment is 388 kips. Shear at the pier is well over 500 kips, so stiffeners will surely be needed for this beam. As an aside, for this web to work as an unstiffened web, its thickness would need to increase to 3/4 in. to work at the pier and 5/8 in. to work near the abutments. An economic comparison of these solutions could be made to determine the most economical solution. The engineer made those calculations and concluded the following:
At the beam ends, a 5/8 in. web could be used as unstiffened, they chose 1/2 in. plus stiffeners.
At the pier sections, a 3/4 in. web works without stiffeners, they chose 9/16 in. and added stiffeners.

## Slide 52: Regions Requiring Stiffeners
Stiffeners are required in the shaded regions, i.e. Vu > 239 kips
Notes: The shaded regions indicate the locations of the beam where a ½ in web would need stiffeners. As mentioned on the prior slide, the engineer then also chose to increase the web thickness in the field sections over the pier to 9/16 in.; these shaded regions near the pier would then be smaller. This is simply used to illustrate the process of identifying regions of the beam that do and do not require shear stiffeners.

## Slide 53: Shear Stiffener Layout
Notes: The layout of the final stiffeners is shown on this slide. A check of several of these locations is provided on subsequent slides.

## Slide 54: End Panel
Maximum distance between bearing stiffener and first intermediate stiffeners is limited to 1.5D = 103.5 in.
Capacity of an end panel is CVp
C is computed with k > 5 for stiffened end panels
Notes: The design of the end panel is the first step. Because the capacity of the unstiffened web is not adequate, stiffeners are needed. Stiffeners must be spaced not to exceed 1.5D in end panels to be considered effective by AASHTO.

## Slide 55: End Panel
Design Example 1 says assume a stiffener placed 87 in. from the abutment bearing stiffener
This would not be an assumed value, it would be back-calculated to meet a target resistance
Notes: The design example states that a stiffener is assumed at 87 in. from the centerline of bearing at the end of the beam. Practically, except by a good guess, an engineer would not assume this value. A guess might be 1.5D, 1D, or something like that to see what resistance is provided. An iteration or two might be used to “guess and check” the location of this first stiffener.

## Slide 56: End Panel
Stiffener spacing, do = 87 in.
Find a new value for C
Notes: With the assumed (or converged) spacing of 87 in. the value for k is computed. This is needed to find a value for C.

## Slide 57: Stiffened Web Capacity
Note: k = 8.15 shifts the unstiffened web resistance curve to the right
The same “slenderness” web has increased resistance due to stiffeners
Chart: C vs D/tw
Notes: A k=8.15 shifts the anchor points of the three regions to the right as compared to the unstiffened web with k=5. The web is still in the elastic buckling region but the value for C is greatly increased due to the presence of stiffeners. C is computed and C=0.390.

## Slide 58: Stiffened Web Capacity
Vn = Vcr = CVp = (0.390)(1001) = 390 kips
φVn = 1.0 Vn = 390 kips > Vu = 388 kips
As mentioned previously, it is unlikely this stiffener spacing was “assumed” but rather found by several trials as the maximum permissible stiffener spacing
Notes: The capacity of an end panel is the lesser of CVp and Vp. Since C=0.39, the web panel is governed by buckling and not yielding. The capacity is simply CVp = 390 kips, compared to the demand of 388 kips. As mentioned previously, it is unlikely that the location of the stiffener was guessed so precisely as to exactly meet the shear demand. A spreadsheet, or some iteration was used to locate this first stiffener.

## Slide 59: First Interior Panel
Remaining distance to first cross-frame is 16’-9”
Check if this spacing is adequate
This is called an “interior panel”, i.e.. it is bounded by web on both sides
Notes: With the first stiffener located 7’-3” from CL bearing, that leaves a remaining 16’-9” to the first cross-frame location. Check if that panel is adequate for shear without needing to further subdivide and add additional stiffeners.

## Slide 60: Shear @ 7’-3” from CL Abutment
The interior panel is designed for the highest shear in the panel
Vu = 345 kips
Notes: The highest shear in the panel is the shear at the location of the previously designed stiffener. It is found by factoring and summing the components of shear due to DL and LL+IM as previously done for the left abutment shear. A factored shear of 345 kips must be resisted in this first interior panel.

## Slide 61: Interior Panel Resistance
Check if full or reduced tension field action, i.e., shear post buckling resistance, can be used
Notes: Prior to computing the shear resistance, determine whether or not full tension field action can be used. The ratio of web and flange areas is computed. Because this ratio is less than 2.5, full tension field action is permitted in this web panel.

## Slide 62: Interior Panel resistance
Find new values for C with do = 201 in.
Notes: The equation for postbuckling resistance / tension field action is provided. The calculation begins with the new do value, 201 in.

## Slide 63: Interior Panel
Stiffener spacing, do = 201 in.
Notes: A new k value is computed for the first interior panel as well as the corresponding value for C.

## Slide 64: Interior Panel resistance
Vn = 475 kips > Vu = 345 kips. Spacing is OK
Notes: With all the needed inputs, the nominal shear resistance is computed. The resistance is 475 kips. This exceeds the highest shear in the panel. No other stiffeners other than the end panel stiffener are needed between the bearing stiffener and the first cross-frame.

## Slide 65: Transverse stiffener requirements

## Slide 66: Transverse Stiffeners
General requirements, LRFD 6.10.11.1.1
  Plates or angles welded or bolted to one or both sides of a web
    Welded single sided plate is the most common, almost 100% use of this detail
  If NOT used as a connection plate can be tight fit to compression flange. Does not need to attach to tension flange
  If it IS used as a connection plate, must attach to both flanges
Notes: General requirements for transverse stiffeners are given in LRFD 6.10.11.1.1. The dominant parameter for an effective stiffener is its stiffness and thus many of the requirements for stiffeners relate to stiffness (moment of inertia).
The LRFD allows for the use of plates welded to one or both sides of the web as well as bolted elements, i.e., an angle, to be used as stiffeners. The use of a single-sided plate is nearly the universal choice. Stiffeners in pairs (double-sided) are common when a diaphragm / cross-frame connection plate to an interior beam is double counted as a shear stiffener.
When a stiffener is used as a connection plate, as shown on this slide, it is required to be in contact and welded / bolted to both flanges. This helps with the rigidity of the connection and prevents distortion-induced fatigue cracking of the web-to-flange weld. This will be addressed in more detail in Lesson 7.
When not used as a connection plate, an example being the end panel stiffener previously designed, the stiffener need only be tight fit to the compression flange, does not need to be welded or bolted to the compression flange, and does not even need to touch the tension flange. LRFD 6.10.11.1.1 requires the weld between the stiffener and web must terminate no more than 6tw or 4 in. from the toe of the flange-to-web weld. This is used to determine the practical gap between a stiffener and the tension flange if they are cut short.
Although there is some evidence of axial stresses in the transverse stiffeners due to tension field action, these effects are relatively minor compared to the lateral loading on the stiffeners due to the postbuckling response of the web panels. The area needed to anchor the vertical component of the tension field is provided by default through stiffeners that meet the stiffness and proportioning requirements.
Image Credit: FHWA

## Slide 67: Transverse Stiffener Requirements
LRFD 6.10.11.1.2 – Projecting width, bt
bf = widest compression flange width in a field section
tp = thickness of projecting stiffener
Notes: Three requirements relate to the width of the stiffener and are shown on this slide. They all relate to providing a stiffener that can fulfill its primary obligation, serve as a lateral support point for the web. The limits enforce these stiffness requirements by requiring stiffeners have a minimum width as compared to the web depth, a minimum width as compared to the flange width, and that they are not too slender such that axial loads induced by the tension field or bending induced by anchoring of the tension field result in buckling of the stiffener plate.

## Slide 68: Transverse Stiffener Requirements
Moment of Inertia, LRFD 6.10.11.1.3
  Various provisions exist for transverse stiffener moment of inertia
  These depend on whether
    Stiffener is bounded by panels without tension field action
    With tension field action
    With longitudinal stiffeners
  Detailed presentation not covered in the class. Refer to the SBDH Vol 4 and Vol 20 (Example 1) for details
Notes: There are numerous requirements that govern the moment of inertia of the stiffener. The reader is referred to SBDH Vol 4 and Vol 20 for further details.

## Slide 69: Guided Walkthrough – Transverse stiffener proportions

## Slide 70: Transverse Stiffener Requirements
LRFD 6.10.11 contains requirements
Projecting width
Also
Use 6 in. (also less than half flange width)
Try 0.5 in. thick
Check b/t < 16 (b/t = 12). Check satisfied
Notes: A transverse stiffener is sized for the SBDH Vol 20 sample design. In the field section near the abutment, the widest compression flange is 16 in. That and the web depth are used to pick a projecting width. The value chosen by the designer is 6 in. Knowing that there is also a minimum thickness check, related to stiffener width, the designer chooses a 1/2 in. thick stiffener plate.

## Slide 71: Transverse Stiffener Moment of Inertia
For detailed checks of the Moment of Inertia requirements, see SBDH Vol 20 (Example 1), Section 10.5.1.2
Required Moment of Inertia = 20.60 in.4
Computed Moment of Inertia about the face of web = = 36.0 in.4 > 20.6, OK
bt
t
Face of web
Notes: The numerous requirements for moment of inertia are computed resulting in a required moment of inertia of 20.6 in^4. The moment of inertia of a single stiffener is defined by AASHTO as being computed about its base. The equation for moment of inertia of a rectangle taken about the base is tb^3 / 3, computed as 36 in^4. The stiffener satisfies all AASHTO requirements.

## Slide 72: Bearing stiffener requirements

## Slide 73: Bearing Stiffeners
General requirements, LRFD 6.10.11.2
  Designed as columns to resist the reactions at bearing locations
  Must be placed on
    webs of built-up sections at all bearing locations
    at bearing locations on rolled shapes and at other locations on built-up sections or rolled shapes subjected to concentrated loads not satisfying the web crippling and yielding provisions of Article D6.5
Notes: LRFD 6.10.11.2 provides the locations in a beam where bearing stiffeners are required. For a typical bridge beam, the only location where concentrated loads are directly applied to the member (i.e.. not through the deck) are where the beams pass over supports and bearings. At those locations, a concentrated vertical reaction is applied to the bottom flange. Bearing stiffeners are then designed as columns with a portion of the web and the stiffeners making up the column cross-section.
Image Credit: FHWA

## Slide 74: Bearing Stiffeners
General requirements continued
  Must extend the full depth of the web and as closely as practical to the outer edges of the flanges
  Must be finished-to-bear against the flange through which it receives its load (i.e., the bottom flange at supports) and attached with fillet welds or by a full penetration groove weld
  Recommended practice uses finish-to-bear plus fillet welds
  Connection to web must transmit all loads to / from the web and bearing stiffeners
Notes: To adequately stiffen the web and prevent local distortions of the flanges, the bearing stiffeners extend as close as practical to the edges of the flanges, the bottom flange usually being the same width or wider than the top flange. The stiffener must be in tight contact with the flange through which it receives its load, typically the bottom flange. This is achieved by a variety of surface preparations including mill-to-bear, grind-to-bear, sawcutting, so that the gap between the stiffener and flange is negligible. When bearing stiffeners also function as connection plates, they must also be welded to the flanges. The common and cost-effective solution is to fillet weld the stiffener to the flanges. An alternate but much more expensive option is to bevel the end of the bearing stiffeners and attach them with complete joint penetration (CJP) welds to the flanges. This offers no structural advantage, and this practice is discouraged due to possible welding distortions of the flange. An additional requirement is that the connection of the bearing stiffeners to the web must be capable of transmitting the entire reaction load to the web. Commonly, when plates are used for the bearing stiffeners, fillet welds run the full height of the plate junction with the web and provide the required load path.

## Slide 75: Bearing Stiffeners
Minimum thickness, LRFD 6.10.11.2.2
bt = the projecting width of the bearing stiffener
tp = thickness of the bearing stiffener
Fys = yield strength of the bearing stiffener
Notes: A minimum thickness requirement is provided. It is a slenderness requirement in that it relates the minimum thickness to the projecting plate width. Recall bearing stiffeners should extend to nearly to the edge of the flange so a width can simply be chosen and then a minimum thickness computed from the above formula.
Image Credit: FHWA

## Slide 76: Bearing Resistance, LRFD 6.10.11.2.3
Where
= 1 and = 1.4ApnFys
Apn = area of bearing stiffeners in contact with the flange
Notes: Having chosen a width, and computed a minimum thickness, the bearing resistance of the stiffeners is checked. The bearing resistance check must reflect the fact that a portion of the stiffener is clipped at the inside corner near the web. This is so that the stiffener can clear the web-to-flange weld needed to assemble the girder. Most owners have standard details for the dimensions of this clip. Dimensions like 1 in. x 1 in. to 1.5 in x 1.5 in. are common in the industry. This clip reduces the gross width of the plate to a net width. The net width and thickness are used to compute the area needed for the bearing check.

## Slide 77: Axial Resistance, LRFD 6.10.11.2.4
Axial resistance per LRFD 6.9.2.1
Assume buckling is out-of-plane
Effective length factor = 0.75, i.e., column height = 0.75D
For the most common case, single plates welded to each side of the web, include 18tw as part of the axial resistance
Notes: An additional check is needed for the axial / compression / column resistance of the stiffener. For this check, the clip is not relevant and the gross section of the plates is used as they describe the stiffness of the section that is prone to buckling.
The only possible buckling mode is for the stiffeners, and a portion of the web, to buckle out-of-plane, i.e.. normal to the axis of the girder. The buckling axis is the centerline of the web. Because of the restraint provided by the flanges to the top and bottom of the stiffener plates, they are not free to buckle like a pinned-end column. A K factor of 0.75 is used for the effective length. So the hypothetical column length for this axial resistance check is 0.75D, D is the web height. Most commonly a bearing stiffener consists of two plates, one on each side. Other variations include a four-plate grouping, pairs of stiffeners. This is when the reactions are very high. Another example of pairs of stiffeners would be an element at an expansion joint where large movements are expected and it is desired to always have stiffeners, more or less centered over the bearing throughout a range of movements. But for the common case of a single pair of stiffeners, AASHTO specifies that the portion of web to be included in the column cross-section be taken as 18tw.

## Slide 78: Axial Resistance, LRFD 6.9.2.1
Yield resistance,
Flexural buckling resistance,
If
Equals 0.877Pe otherwise
Chart: Column Axial resistance
Notes: For axial resistance, the designer is referred to LRFD 6.9.2.1. Several parameters are needed to compute the design resistance. These are: the yield resistance, Po, the flexural buckling resistance, Pe, and the nominal resistance. A plot of the classic column resistance curve as a function of column slenderness, Kl/r is provided. The plot depicts the slenderness of the column on the horizontal axis and the vertical axis is the fraction of the yield resistance, Po, that can be achieved, i.e.. Pn/Po. Recall K=0.75 for the assumed restrained condition at the flanges, l is the web height, and r is the radius of gyration with the moment of inertia being of the effective section of the web and stiffener pair taken about the centerline of web.

## Slide 79: Guided Walkthrough – Bearing stiffeners

## Slide 80: Abutment Bearing Stiffener
Reaction, Ru = 388 kips
Extend bearing stiffeners near tips of narrowest flange (16 in.). Assume 7 in. each
Minimum width,
Try a 5/8 in. thick stiffener
Notes: The abutment reaction at the STR I limit state is 388 kips. An assumed plate width is chosen based on flange geometry and the minimum thickness is established. This trial stiffener, 7 x 5/8 in. is then used to check the bearing and axial resistance.

## Slide 81: Bearing Resistance
Where
= 1 and = 1.4ApnFys
Apn = 2(7.0-1.5)(0.625) = 6.88 in.2
= 1.4(6.88)(50) = 482 kips > Ru = 388, OK
Notes: The net width of the bearing stiffeners is computed assuming a 1.5 in corner clip in each stiffener. Note that for the bearing check, the web area is neglected. All load is assumed to come through the milled surface of the bearing stiffener and the bottom flange. The bearing check is satisfied.

## Slide 82: Axial / Column resistance
Check the axial resistance of the column
Column consists of projecting stiffeners + a centrally located strip of web as shown
A = 18tw2 = 4.5 in.2 for the web plus (2)(7)(0.625) = 8.75 in.2 for 2 stiffeners = 13.25 in.2
Notes: A column section consisting of the outstanding plates and a centrally located strip of web is assumed for the axial resistance checks. The area is computed as 13.25 in.2

## Slide 83: Axial / Column resistance
Compute the moment of inertia computed about the centerline of the web
It is conservative to only use the stiffeners since the web Moment of Inertia about its own midplane is nearly zero
3.46 in.
Notes: The moment of inertia is computed using the traditional equation for a rectangular section, bh^3 / 12 where b=stiffener width and h=the width of two stiffeners plus the 0.5 in allowance for the web between the stiffeners. The moment of inertia of the web is neglected. It is a thin plate whose moment of inertia about its own mid-plane is nearly zero due to the cubing of the 0.5 in dimension. The radius of gyration is computed using the conventional formula.

## Slide 84: Axial / Column resistance
For buckling, a column is assumed to be 75% of the web height, i.e., k=0.75. So kL = 0.75 * 69 = 51.75 in.
Compute the Elastic Buckling resistance as
kips
Compute the nominal yield resistance
Po / Pe = 0.04, less than 2.25
Notes: The axial resistance is computed using the provisions of LRFD 6.9.2.1. The column length is 0.75D. The area and radius of gyration needed for calculation of the flexural buckling resistance are taken from the prior slide. Note that due to the very short length of this section, the buckling resistance is nearly 17,000 kips. This is a fictitious number in the sense that the material can never support this load. In fact, the compression resistance of the material cannot exceed Fy. This is the calculation of the value Po, 662 kips, assuming the stress on the cross-section approaches yield. Due to the short, but not zero, unbraced length, the section can not fully reach the yield capacity.

## Slide 85: Axial / Column resistance
Po / Pe = 0.04, less than 2.25, therefore
For compression in columns, φ = 0.9
φPn = 0.9(651) = 618 Kips, Ru = 388 kips, OK
Notes: With a yield capacity of 662 kips and buckling capacity of 16,920 kips, the ratio of Pe/Po is 0.04, much less than 2.25. That means this column buckles inelastically and the capacity is computed as 651 kips. Recall the factored reaction at the abutment is 388 kips. The bearing stiffener meets all specification requirements and is satisfactory for the design loads.

## Slide 86: Lesson 5 Summary
Review of influence line loading
Basics of shear resistance
LRFD shear resistance
Guided walkthrough for rolled shape and plate girder resistance
Design and detailing of shear and bearing stiffeners
Notes: Summary of lesson topics:
Influence lines for end and interior support shear were presented along with example load positioning to maximize or minimize the shear forces.
The fundamentals of shear resistance were presented. Shear resistance comes from either yielding or buckling. Tension field action resistance was introduced.
The LRFD provisions for shear resistance are provided. End and interior panel design approaches are presented.
Application of the LRFD resistance equations is demonstrated for a rolled shape and a stiffened plate girder panel.
Design and detailing for shear and bearing stiffeners was presented.

## Slide 87: END